New Build Vessel

All sections of this questionnaire should be submitted to BP Shipping (vetting@bp.com) not earlier than 5 days before delivery of the vessel.

Acquisition of Existing Vessel into Management

All sections of this questionnaire should be submitted to BP Shipping (vetting@bp.com) on or after taking delivery of existing vessel from previous managers.

In both scenarios, the ‘Post Delivery Checklist’ contained in the ‘Appendix’ is to be completed.

Please note that when submitted, it will be electronically stored and may be assessed as part of the normal screening process if the vessel is to be considered for BP operations.

Section 1: General Information

Vessel Name

IMO Number

ENI or VIN Number	 (If applicable)

Vessel Flag

Classification Society

P&I  Club

Confirm that US $1 Billion Pollution Liability Cover is in place with the P&I club identified above

Yes

No

If ‘NO’, please state Pollution Liability Cover amount and name of insurer

Electronic Chart Display and Information System (ECDIS)

Vessel fitted with ECDIS 	Yes

Maker/Model	    Quantity

No

If ‘NO’, please state reasons

Primary means of navigation

Secondary means of navigation

Backup (MSC 1 Circ 1496) stipulated in Safety equipment certificate form E;

Delivery Date (New Build)	(dd/mm/yyyy)

Handover to new managers	 (dd/mm/yyyy)

(Takeover of existing vessel)

Technical Manager

IMO Number

Vessel Manager

IMO Number

DOC Company

IMO Number

Commercial Operator

Registered Owner

Group Owner

Section 2: Declaration

DRILLS

All required drills as per SOLAS, carried out satisfactorily following delivery / change of management

Yes

Date  (dd/mm/yyyy)

No

If ‘NO’, please state reasons

SOLAS Charts/Publication

Charts and nautical publications required by SOLAS are corrected to latest available Notices to Mariners.

Yes

No

If ‘NO’, please state reasons

Management of Change (MoC)

MoC for new delivery / change of managers carried out and completed satisfactorily

Yes (Kindly furnish a copy for our review and records)

No

If ‘NO’, please state reasons

Vessel Information update

Has the vessel undergone any major hull or type of vessel conversion?

No

Yes

Date of conversion   (dd/mm/yyyy)

If ‘YES’, please give details

Has the following information uploaded?

HVPQ to OCIMF	Yes	 No

Lloyd’s Fairplay (IHS) 	Yes	 No

Online Crew Matrix	Yes	 No

Person In-Charge

Name

Designation

Address

Telephone

Fax e.g. 441932775326

Email

Warranted Correct by

Name and position Held

Company Name

Appendix

Appendix:

BP Shipping Post Delivery Checklist

Vessel Name	:

IMO Number	:

Delivery Date	: (dd/mm/yyyy)

Date start of Check List	: (dd/mm/yyyy)

Date completed Check List	: (dd/mm/yyyy)

Introduction

The “shakedown” process is a method of proving good many of the ship’s systems that have been delivered into service with potentially serious unknown defects.  When tested separately in the commissioning stages, these systems performed and met requirements.  When tested operationally and in many cases where they form part of other systems, defects have been found.  A member of the ship’s officers or engineers must be present during these tests.

On this basis, the following list of commissioning tests are to be undertaken.

The following activities are to be undertaken:

| Test | Confirmed |
| --- | --- |
| Testing of ships fire detection system – ensure there are no delays between activation and the bells sounding | Yes / No / NA |
| Confirm the automatic door release mechanisms operational on fire doors where fitted | Yes / No / NA |
| Carry out an emergency muster and a boat muster – statutory requirement within 24 hours of taking over. | Yes / No / NA |
| Run the emergency fire pump, charge one hose and prove system operational | Yes / No / NA |
| Run the accommodation at-will hoses and prove good if applicable | Yes / No / NA |
| Check that the main engine room fixed fire extinguishing system is on automatic and ready to release whether it be CO2, flexi fog etc. | Yes / No / NA |
| Check the foam tank and fire valves are correctly set | Yes / No / NA |
| (Gas Vessels) Check the fixed Dry Powder stations on deck are ready to go | Yes / No / NA |
| Check the local firefighting capability for generators etc. is in operational readiness in auto. | Yes / No / NA |
| Confirm location of the bilge injection valve and label accordingly | Yes / No / NA |
| Run the emergency generator on auto start and confirm it takes load | Yes / No / NA |

When it is confirmed that the above safety critical systems are in operational readiness, the remaining checks on the following pages (Part 1, 2 and 3) are to be carried out.

Pre-departure

| SHIP EQUIPMENT CHECK LIST | STATUS |
| --- | --- |
| 1 | Date of test | MAIN POWER UNIT (STEAMSHIPS) |  |
|  |  | Vacuum pumps/air ejector operating within normal parameters | Yes / No / NA |
|  |  | Lubricating oil system | Yes / No |
|  |  | Manoeuvring Valves operating freely and steam tight when Closed |  |
|  |  | Auto Spin function tested and working correctly | Yes / No |
|  |  | Turning Gear Interlock function tested | Yes / No |
|  |  | Gland steam system operating satisfactorily during M/E use and stand still modes | Yes / No |
|  |  | PPM of Main Condenser outlet within normal range, SW system and vacuum satisfactory | Yes / No |
|  |  | Salinometer system in working order and reading accurately | Yes / No |
|  |  | All steam feed and exhaust system control valves operating satisfactorily | Yes / No |

| 2 | Date of test | MAIN POWER UNIT (MOTOR SHIPS) |
| --- | --- | --- |
|  |  | Fuel Oil System: |  |
|  |  | Is the system functioning normally and maintaining fuel temperature within normal range | Yes / No |
|  |  | Is system pressure maintained within normal range during engine operation and stand still conditions | Yes / No |
|  |  | LO Pressure Satisfactory | Yes / No |
|  |  | FW Cooling Systems Satisfactory | Yes / No |
|  |  | Main engine air compressors operational and satisfactory | Yes / No |
|  |  | Main engine air start system leak free | Yes / No |
|  |  | Main engine control air system leak free | Yes / No |

| Date of Test | Main Power Unit Diesel Electric Dual fuel propulsion |
| --- | --- |
| Dual Fuel Diesel Electric – Main Generators |
|  | Oil Mist Detector function Tested | Yes/No | Yes/No | Yes/No | Yes/No |
|  | L.O. Low Pressure Alarm and Trip Tested | Yes/No | Yes/No | Yes/No | Yes/No |
|  | Turning Gear Interlock Functions | Yes/No | Yes/No | Yes/No | Yes/No |
|  | HT Cooling water outlet high temp. trip. Tested | Yes/No | Yes/No | Yes/No | Yes/No |
|  | Local Operation | Yes/No | Yes/No | Yes/No | Yes/No |
|  | Slow turn function operates correctly | Yes/No | Yes/No | Yes/No | Yes/No |
|  | Gas to Diesel trip – Unit temp deviation (if possible) | Yes/No | Yes/No | Yes/No | Yes/No |
|  | Gas to Diesel trip – Main gas pressure low (if possible) | Yes/No | Yes/No | Yes/No | Yes/No |
| Dual Fuel Diesel Electric – Propulsion Systems |
|  | Gearbox L.O. system operation | Yes / No |
|  | Gearbox L.O. system trips Tested | Yes / No |
|  | Stern Tube seal system and drains | Yes / No |
|  | Shaft locking device & Towing procedure produced | Yes / No |
|  | Procedure for single motor propulsion in place | Yes / No |
|  | Run both PEM’s on one transformer | Yes / No |

| 3 | Date of test | MAIN POWER UNIT (GENERAL) |
| --- | --- | --- |
|  |  | Engine Manoeuvring System Satisfactory | Yes / No |
|  |  | Commissioning letter received confirming NCR/MCR conditions | Yes / No |
|  |  | Stern tube system oil levels normal and sealing arrangement leak free | Yes / No |
|  |  | M/E Alarms & Trips tested and working satisfactorily | Yes / No |
|  |  | Aux blowers operating normally | Yes / No |
|  |  | Control air compressors satisfactory (Check cut in/out frequency) | Yes / No |
|  |  | Turning Gear interlock function test | Yes / No |
|  |  | Shaft Generator function test | Yes / No / NA |
|  |  | Power takeoff mode (PTO) | Yes / No / NA |
|  |  | Power Take in mode (PTI) | Yes / No / NA |
|  |  | Clutch assembly for main shaft / CPP operational | Yes / No / NA |
|  |  | First Start Arrangement satisfactory | Yes / No |
|  |  | Test all starting arrangements for Emergency genset | Yes / No |

| Date of test | Gas Combustion Unit |
| --- | --- |
|  | Verify operation of GCU master trip | Yes / No |
|  | Verify wheelhouse inhibit switch operational | Yes / No |
|  | GCU Combustion fans operational | Yes / No |
|  | GCU Dilution air fans operational | Yes / No |
|  | Verify normal auto operation of GCU | Yes / No |
|  | Check purge air supply to diesel igniter | Yes / No |

| Date of test | Nitrogen Plant and N2 compressors |
| --- | --- |
|  | Verify operation of #1 N2 compressor in auto | Yes / No |
|  | Verify operation of #2 N2 compressor in auto | Yes / No |
|  | N2 gas leakage alarm | Yes / No |

| Date of test | Inert Gas Generator & Drying Plant |
| --- | --- |
|  | Verify IGG full auto operation | Yes / No |
|  | Verify Drying plant full auto operation | Yes / No |
|  | Test CSW no flow trip – IGG | Yes / No |
|  | Test High O2 recirculation valve operational – IGG | Yes / No |
|  | Confirm operation of O2 content monitor - IGG | Yes / No |
|  | Confirm operation of dew point meter – Drying plant | Yes / No |
|  | Confirm adequate calibration gas available onboard | Yes / No |
|  | Emergency stop trip tested | Yes / No |

| Date of test | Gas Detection system |
| --- | --- |
|  | Confirm GAS detection system activates alarms with no delay | Yes / No |
|  | Test fuel gas master valve trip for GAS detected | Yes / No |

| Date of test | Inert Gas Drying Plant and IGG Blowers |
| --- | --- |
|  | Both IGG blowers operational | Yes / No |
|  | Drying plant operational in auto | Yes / No |
|  | Air heating plant operational in auto | Yes / No |

| 4 | Date of test | STEAM PLANT |
| --- | --- | --- |
|  |  | Integrity of Steam system satisfactory (list defects) | Yes / No |
|  |  | Integrity of Feed system satisfactory (list defects) | Yes / No |
|  |  | Feed water regulators functioning normally | Yes / No |
|  |  | Water level indicators satisfactory | Yes / No |
|  |  | Control Equipment Satisfactory: |  |
|  |  | Flame failure alarms and trips | Yes / No |
|  |  | Low and High water level alarms and trips operating satisfactorily | Yes / No |
|  |  | Burner operation satisfactory | Yes / No |
|  |  | Integrity of Fuel system satisfactory (list defects) | Yes / No |
|  |  | Manual fuel trips tested and satisfactory | Yes / No |
|  |  | FO pump remote stops operating | Yes / No |
|  |  | FD fan remote stops operating | Yes / No |
|  |  | FD Fans Operating Satisfactorily | Yes / No |
|  |  | Boiler casings free from gas leaks (list defects) | Yes / No |
|  |  | Test fire boiler in all operating modes | Yes / No |

| 5 Date of test | Thermal Oil system |
| --- | --- |
|  | Operation test | Yes / No / NA |
|  | Alarms and Trips | Yes / No / NA |

| 6 Date of test | Bow Thruster |
| --- | --- |
|  | Operation test, port and starboard thrust and idle position | Yes / No / NA |
|  | Emergency Stop | Yes / No / NA |

| 7 | Date of test | DISTILLING PLANT |
| --- | --- | --- |
|  |  | Plant working satisfactorily and producing rated output | Yes / No |
|  |  | Water meters operative | Yes / No |
|  |  | Adequate distilled and fresh water reserves on board on sailing | Yes / No |

| 8 | Date of test | HULL OPENINGS |
| --- | --- | --- |
|  |  | All shipside valves opening and closing freely | Yes / No |

| 9 | Date of test | MOORING AND LIFTING EQUIPMENT |
| --- | --- | --- |
|  |  | Windlass and attachments in good order – Raise / Lower anchors | Yes / No |
|  |  | Capstans in good working order | Yes / No / NA |
|  |  | Deck winches in good working order | Yes / No |
|  |  | Engine room cranes operating satisfactorily | Yes / No |
|  |  | Stores cranes operating satisfactorily | Yes / No |
|  |  | Cargo hose davit/crane operating satisfactorily | Yes / No |

| 10 | Date of test | ELECTRICAL SUPPLY |
| --- | --- | --- |
|  |  | Switchboard meters operating satisfactorily | Yes / No |
|  |  | All AVRs operating | Yes / No |
|  |  | Reverse power trips operational and tested | Yes / No |
|  |  | Generators’ Overspeed trips operational and tested | Yes / No |
|  |  | Governor controls operational and tested | Yes / No |
|  |  | Alternators operating in parallel – operate satisfactorily | Yes / No |
|  |  | Power Management System fully operational | Yes / No |
|  |  | All alarms and trips tested and satisfactory – switchboard | Yes / No |
|  |  | HV Electrical system |  |
|  |  | Ensure all cubicles are secure and keys located in appropriate key boxes or locks | Yes / No |
|  |  | Ensure all tools and test gear for HV system identified and batteries charged where appropriate | Yes / No |
|  |  | Ensure access to rear of HV switchboards locked | Yes / No |
|  |  | Ensure EARTHING truck is located in the appropriate cubicle on each switchboard pair (CSB and MSB) | Yes / No |
|  |  | Ensure Electric shock posters displayed in all switchboard rooms in a clear visible position | Yes / No |
|  |  | Ensure door sign on access doors to HV switchboard rooms is present. E.g. High Voltage, No unauthorised Access permitted. | Yes / No |
|  |  | Blackout Test | Yes / No |
|  |  | Preference and overcurrent alarms and trips | Yes / No |
|  |  | Sequential starts operating normally | Yes / No |
|  |  | All lighting tested / Navigation / Signal / Flood / External Accommodation | Yes / No |
|  |  | Insulation levels 5M ohms or on all section board Meters | Yes / No |
|  |  | Emergency batteries secure for GMDSS/UPS systems & lifeboat. | Yes / No |

| 11 | Date of test | NAVIGATIONAL EQUIPMENT |
| --- | --- | --- |
|  |  | All equipment’s and associated systems operating satisfactorily | Yes / No |
|  |  | Steering gear changeover, emergency arrangements, communications and alarms tested and satisfactory, procedure in place. | Yes / No |
|  |  | Whistles and controls operating satisfactorily | Yes / No |
|  |  | Radar/ARPA/ECDIS fully operational – shadow diagrams posted | Yes / No |
|  |  | Gyro compasses satisfactory | Yes / No |
|  |  | Magnetic Compass satisfactory – Compass deviation card posted | Yes / No |
|  |  | Doppler / Electro-magnetic Log satisfactory | Yes / No |
|  |  | Echo Sounder satisfactory and both transducers operational | Yes / No |
|  |  | GPS receivers displaying correct position | Yes / No |
|  |  | DSAS unit switched on and CSO informed | Yes / No |
|  |  | GMDSS equipment satisfactory | Yes / No |
|  |  | Engine Order Recorder operating satisfactorily | Yes / No |
|  |  | VDR switched on at delivery and operational | Yes / No |
|  |  | AIS system switched on an operational | Yes / No |
|  |  | Miscellaneous Instruments operating satisfactorily, weather fax, rudder angle indicator, wind anemometer, etc. | Yes / No |
|  |  | Check operation of ships PA system | Yes / No |
|  |  | Check operation of master clock | Yes / No |
|  |  | Check operation of bridge window wipers | Yes / No |
|  |  | VHF self-test | Yes / No |

| 12 | Date of test | MISCELLANEOUS |
| --- | --- | --- |
|  |  | Incinerator operating satisfactorily | Yes / No |
|  |  | Function test of Inert Gas System, inert gas to be vented to deck for 30 minutes with less than 5% O2 produced. This test to be run in conjunction with function test | Yes / No / NA |
|  |  | Inert Gas Generator (LPG): | Yes / No / NA |
|  |  | COT IG pressure, CHECK THERE ARE NO BLANKS BY: |  |
|  |  | Press up TK’s with IG or fresh air and prove pressure in all tanks | Yes / No / NA |
|  |  | Vent COT pressure thru Hi-jets or riser and prove each TK is clear. | Yes / No / NA |
|  |  | Operation satisfactory (O2 & dew point values ok) | Yes / No |
|  |  | Alarms & Trips Scrubber cooling water no flow trip Flame fail | Yes / No |
|  |  | Sewage treatment plant on line and operating satisfactorily | Yes / No |
|  |  | Bilge system tested internally | Yes / No |
|  |  | OWS – function test of 3-way valve and alarm proven | Yes / No |
|  |  | F.O & L.O purifier plant in operation and operating in required temperature range without problem | Yes / No |
|  |  | General cleanliness of machinery spaces, power plant and auxiliary machinery satisfactory | Yes / No |
|  |  | Bilge Injection valve opened and closed | Yes / No |
|  |  | Gas Detection system on and operational, at least one sensor to be tested | Yes / No |
|  |  | LNG & LPG VESSELS |  |
|  |  | Check all fixed dry power stations are ready for use | Yes / No |
|  |  | Barrier spaces, check IS and IBS N2 system | Yes / No |
|  |  | Check nitrogen shaft seal integrity on cargo compressors | Yes / No |
|  |  | Bilge alarms: |  |
|  |  | Engine room | Yes / No |
|  |  | Pump room | Yes / No / NA |
|  |  | Forecastle | Yes / No / NA |
|  |  | Motor Room | Yes / No / NA |
|  |  | Compressor Room | Yes / No / NA |
|  |  | Purge air system for manifold blowing | Yes / No |
|  |  | Check and padlock / lash all IG isolation valves on deck | Yes / No |
|  |  | Check and padlock pump room overboard valves as required | Yes / No |
|  |  | Secure all drain plugs to save-alls | Yes / No |
|  |  | Inspect all gauge glasses and remove any gags | Yes / No |
|  |  | Loading Computer, check ullages / soundings | Yes / No |
|  |  | ER Annular pipe purge system fan stop trips FG master valve | Yes / No |

| 13 | Date of test | GALLEY SAFETY EQUIPMENT |
| --- | --- | --- |
|  |  | Co2 Extinguishing System for Galley Duct inspected and ready for use. | Yes / No |
|  |  | Wet Chemical Fire Extinguisher for Deep Frying Machine inspected and ready for use | Yes / No |
|  |  | Cold Chambers Alarm tested and temperature satisfactory | Yes / No |
|  |  | Portable Fire Extinguisher in place | Yes / No |
|  |  | Fire Blanket Fitted | Yes / No |

| 14 | Date of test | GALLEY ELECTRICAL APPLIANCES – FUNCTION TEST |
| --- | --- | --- |
|  |  | Main Range | Yes / No |
|  |  | Baker’s Oven | Yes / No |
|  |  | Combination Oven | Yes / No |
|  |  | Dough Mixing Machine | Yes / No |
|  |  | Salamander Grill | Yes / No |
|  |  | Microwave Oven (Test Door Seal For Leakage) | Yes / No |
|  |  | Deep Frying Machine | Yes / No |
|  |  | Dish Washing Machine | Yes / No |
|  |  | Potato Peeling Machine | Yes / No |
|  |  | Waste Disposal Unit | Yes / No |
|  |  | Refrigerator | Yes / No |
|  |  | Deep Freeze Unit | Yes / No |
|  |  | Griddle Plate | Yes / No |
|  |  | Water Boilers | Yes / No |
|  |  | Galley Air Conditioning Unit (dedicated unit) | Yes / No |
|  |  | Supply Fans | Yes / No |
|  |  | Exhaust Fans | Yes / No |

| 15 | Date of test | GALLEY FITTINGS |
| --- | --- | --- |
|  |  | Doors and Drawers on All Fitted Units Operate Correctly | Yes / No |
|  |  | Anti-roll Bars on Main Range Fit Correctly | Yes / No |
|  |  | Scupper Covers Fit Correctly | Yes / No |

| 16 | Date of test | ACCOMMODATION |
| --- | --- | --- |
|  |  | All Fixed Fittings in Place | Yes / No |
|  |  | Sanitary Extraction Fan Effective | Yes / No |
|  |  | Lifejacket | Yes / No |
|  |  | ELSA / EEBD Set | Yes / No |

| 17 | Date of test | LAUNDRY ROOMS |
| --- | --- | --- |
|  |  | Washing Machines – Function Test | Yes / No |
|  |  | Drying Machines – Function Test | Yes / No |
|  |  | Hydro Extractor – Function Test | Yes / No / NA |
|  |  | Portable Laundry Equipment Supplied | Yes / No |
|  |  | Lighting | Yes / No |
|  |  | Deck Covering | Yes / No |
|  |  | Room Heater (Drying Room) – (function test) | Yes / No |

| 18 | Date of test | SAFETY EQUIPMENT |
| --- | --- | --- |
|  |  | Fire detection system proven and random heads tested – no delays on bells | Yes / No |
|  |  | Fire door magnet switches release on fire alarm activation | Yes / No / NA |
|  |  | Emergency fire pump satisfactory in ballast condition | Yes / No |
|  |  | Deluge system tested | Yes / No |
|  |  | Fan dampers/flaps satisfactory | Yes / No |
|  |  | Fixed Fire Fighting Installations inspected / tested where appropriate and left enabled (including paint locker), Keys placed in boxes next to cabinets, leaded seals intact | Yes / No |
|  |  | CO2 (check blanks swung to open position) | Yes / No / NA |
|  |  | Dry powder | Yes / No |
|  |  | Foam | Yes / No |
|  |  | Flexfog / Watermist | Yes / No / NA |
|  |  | CABA compressor operation proven and cylinders charged, oil filled and air filter fitted prior to charging bottles | Yes / No |
|  |  | Lifeboat tested in-water | Yes / No |
|  |  | Rescue boat tested in-water | Yes / No |
|  |  | Local Procedure in place for lifeboat/rescue boat deployment | Yes / No |
|  |  | Fire Hydrants and Hoses satisfactory | Yes / No |
|  |  | All other fire-fighting and LSA equipment proved and deployed | Yes / No |
|  |  | Accommodation fire-fighting system satisfactory | Yes / No |
|  |  | Fire extinguishers satisfactory, including spares | Yes / No |
|  |  | Emergency stop switches tested satisfactory | Yes / No |
|  |  | Emergency shut off valves tested satisfactory | Yes / No |
|  |  | Fan interlocks proven | Yes / No |
|  |  | Padlocks to be removed from all safety gear stowage boxes | Yes / No |
|  |  | Rescue Boat fuel tank filled (Petrol & 2 stroke Oil supplied as applicable) | Yes / No |
|  |  | Lifeboat fuel level checked and air cylinders fully charged | Yes / No |
|  |  | Foam level satisfactory in Foam tank | Yes / No / NA |
|  |  | CABA & EEBD cylinders fully charged | Yes / No |
|  |  | N2 purging system for tanks & risers ok (LPG) | Yes / No |

| 19 |  | OWNERS SUPPLY OUTFIT |
| --- | --- | --- |
|  |  | BA Compressor |
|  |  | Cooling water chemical dosing system |
|  |  | Boiler soot dosing system |
|  |  | Galley outfit |
|  |  | Laundry outfit |
|  |  | Electrical outfit |
|  |  | Deck outfit |
|  |  | Machinery Outfit |

| 20 |  | SHIPYARD SUPPLY SPARE PARTS AND SPECIAL TOOLS |
| --- | --- | --- |
|  |  | Check all tools in place on Main Engine tool boards | Yes / No |
|  |  | Confirm that all outfit spares boxes contents have been checked off. | Yes / No |

| Section sign off Name /Rank (Print) :…………………………………………………………… Sign :……………………………………………………………. | Date : |
| --- | --- |

| 21 |  | STAFF (to be completed by Master & C/E) |
| --- | --- | --- |
|  |  | Full complement |
|  |  | Are there any concerns from Shipboard Management Team with regards to competencies and experience of staff appointed to the vessel |
| 22 |  | Any outstanding defects which the Master and Chief Engineer consider should be dealt with before the vessel sails: |

| 23 |  | Confirm agreement that vessel is ready to sail |
| --- | --- | --- |
|  |  | …............................................. | …............................................. |
|  |  | Master | Chief Engineer |
|  |  | Delivery Superintendent | Operating Superintendent |
|  |  | Shipping Technical Group (STG) |  |